## Slide 1
Next Level of Evolution in PD Technology
Pulp Dryer Solutions
Johann Resl
August 2025

## Slide 2: References past 10 years
17234 | 19-Dec-14 | 13-Mar-15 | International Paper Co. | Saint-Junien Cedex | France | PD 1 | EMEA | Market Pulp
17237 | 18-Feb-15 | 08-May-15 | ENCE Group | Navia | Spain | PD 3 | EMEA | Market Pulp
15844 | 25-Nov-15 | 01-Jan-16 | Stora Enso Oyj | SKUTSKÄR | Sweden | PD 9 | EMEA | Market Pulp
17277 | 21-Dec-15 | 01-Apr-16 | Fibria | Tres Lagoas | Brazil |  | Americas | Market Pulp
17282 | 21-Dec-15 | 01-Apr-16 | Fibria | Tres Lagoas | Brazil |  | Americas | Market Pulp
17304 | 15-Jul-16 | 28-Oct-16 | Stora Enso Oyj | Kotka | Finland | KK 6 | EMEA | Market Pulp
12200 | 24-Oct-16 | 02-May-17 | SCA Graphic Sundsvall AB | Timra | Sweden | PD 6 | EMEA | Market Pulp
15435 | 15-Dec-16 | 05-Jun-17 | Copamex, S.A. de C.V. | San Nicolas De Los Garza | Mexico | MP 2 | Americas | Market Pulp
18129 | 28-Mar-17 | 10-Jul-17 | Stora Enso Oyj | Uimaharju | Finland | PD 2 | EMEA | Market Pulp
18353 | 28-Mar-17 | 28-Feb-18 | Stora Enso Oyj | Uimaharju | Finland | PD 2 | EMEA | Market Pulp
17506 | 26-Mar-18 | 02-Jul-18 | Celulosa Arauco y Constitucion SA | Valdivia | Chile | PD 1 | Americas | Market Pulp
18528 | 20-Jun-18 | 30-Sep-18 | Mondi | Štetí | Czech Republic | PD 1 | EMEA | Market Pulp
18247 | 28-Sep-18 | 21-Jan-19 | Sun Paper Holding Lao Co Ltd | Savannakhet | China | PD 1 | Asia-Pacific | Market Pulp
17710 | 15-Mar-19 | 01-Jun-19 | Nippon Paper Industries Co Ltd | Suita | Japan |  | Asia-Pacific | Market Pulp
19037 | 02-Dec-19 | 27-Mar-20 | Jiangsu Xingguang New Material Technology Co Ltd | Xuzhou | China | PM 6 | Asia-Pacific | Market Pulp
18723 | 22-Feb-20 | 31-Jul-20 | Bracell | Lençois Paulista | Brazil | PD 2A | Americas | Market Pulp
18724 | 22-Feb-20 | 31-Jul-20 | Bracell | Lençois Paulista | Brazil | PD 2B | Americas | Market Pulp
17727 | 14-Apr-20 | 04-Sep-20 | Iwaki Daio Paper | Iwaki | Japan | PD | Asia-Pacific | Market Pulp
18745 | 23-Sep-20 | 15-Jan-21 | Fedrigoni SpA | Fabriano | Italy | PM 6 | EMEA | Market Pulp
19418 | 01-Apr-22 | 05-Jan-23 | Suzano de Papel e Celulose. | Sao Paulo | Brazil | PD 1 | Americas | Market Pulp
19419 | 01-Apr-22 | 05-Jan-23 | Suzano de Papel e Celulose. | Sao Paulo | Brazil | PD 2 | Americas | Market Pulp
19441 | 02-Feb-23 | 30-Aug-23 | Andritz China Ltd | Fo Shan | China | Line 4 | Asia-Pacific | Pulp
19442 | 02-Feb-23 | 31-Aug-23 | Andritz China Ltd | Fo Shan | China | Line 3 | Asia-Pacific | Pulp
19733 | 03-Feb-23 | 03-Aug-23 | Liansheng Pulp & Paper (Zhangzhou) Co., Ltd. | Zhangzhou | China | PD 1 | Asia-Pacific | Pulp
19734 | 03-Feb-23 | 03-Aug-23 | Liansheng Pulp & Paper (Zhangzhou) Co., Ltd. | Zhangzhou | China | PD 2 | Asia-Pacific | Pulp
19973 | 18-Oct-24 | 28-Mar-25 | Shandong Kaixin Heavy Machinery Co., LTD | Weifang | China | PD 2 | Asia-Pacific | Market Pulp
8508 | 25-Oct-24 | 27-Jul-25 | Borregaard AS | Sarpsborg | Norway | PD | EMEA | Market Pulp

## Slide 3: Experion MX Overview
ExperionMX Server Engineering Station
DCS
Inner Loops for
MD-Controls
Mill Water Supply
Blower, Filter
MD Dilution Control
BW, Dry Stock, Moi, Dryer Shutdown, Jet to Wire,
Switching Hub
Thin Client Station
ProFlow 55+1
CD-Controls
Sr90 BW, Z Sensor, MW Moisture, Color Sheet Temp,
Steam Box 33+1
CD-Controls
OPC-DA
Inbound
traffic ONLY
4G Routerport
Outbound
traffic ONLY
AMQP – Advanced Message Queuing Protocol
Sentience
Cloud Historian
Secured Data
Edge Device
Embedded PC
Option

## Slide 4: Scanners

## Slide 5: Precision Platform 4022 up to 6m Web Width
Fast, Precise Measurement
Compact
Reliable Performance
Easy Maintenance
Notes: 2
To the presenter:
This slide is the “single slide presentation” you might use if asked for a brief overview of the 4022-10 scanner. It can also be used as an overview or outline for this presentation.
Comments:
Scanner is shown in photograph.
Compact
Cost-effective (low cost)
Supports all of Honeywell’s PrecisionPLUS scanning sensors (except Extensional Stiffness)
Provides all PrecisionPLUS measurement features, including
  100% Signal Integration
  Edge Measurement
  Fast Scan for fast profile measurement,
  Parallel Profile Processing,
  ZOOM High Resolution Profiles,
  ZOOM MD Fast MD measurement

## Slide 6: EnviroPak Sensor Enclosure
Accuracy and Reliability Features:
  Air-tight single-plane seals
  Instrument-air purge
  Insulated covers
  Internal air circulation
  Temperature control to ± 1° C (± 1.8° F)
Electromagnetic Interference Protection
Electrostatic Discharge Protection
Sensor Environment for Accurate, Reliable Measurement.
Notes: 10

## Slide 7: Precision Data Acquisition & Signal Processing
Volts / sample
Volts
Head position
(100 Hz read rate)
Database
CD offset from master sensor
Sensor Tc
Sensor spot size
-10 volts
10 volts
32,768 levels at 10 volts (full signal)
328 levels at 0.1volt (1% of full signal)
16 bit resolution
(15-bits for 0 - 10 volts)
Avg. volts / measurement zone
PrecisionNet
Eng Units / measurement zone
“Now” Measurement Zone Profile
Eng Units / Meas. Zone
Volts
Da Vinci Application Server
Precision Measurement Processor
Samples allocation to measurement zones
Anti-alias filter
4000 samples / sec
2 - 5 mm
Precision Sensor analogue outputs

## Slide 8: Universal PMP
Next generation scanner interface
  Utilizes Honeywell’s multipurpose Ethernet Data Acquisition I/O board which was developed for the Experion MX Q4000-80 scanner
  Avoids commercial computing hardware to extend supportable lifespan
Supports current (except Q4000-80), and most legacy, scanners and sensors
Drop in replacement for legacy internal and remote PMPs with obsolete electronics
  Avoids labor intensive, high risk, “box of parts” upgrade from ISA to PCI

## Slide 9: Q4000 Scanner over 6m Web Width
Notes: 2
To the presenter:
This slide is the “single slide presentation” you might use if asked for a brief overview of the 4022-10 scanner. It can also be used as an overview or outline for this presentation.
Comments:
Scanner is shown in photograph.
Compact
Cost-effective (low cost)
Supports all of Honeywell’s PrecisionPLUS scanning sensors (except Extensional Stiffness)
Provides all PrecisionPLUS measurement features, including
  100% Signal Integration
  Edge Measurement
  Fast Scan for fast profile measurement,
  Parallel Profile Processing,
  ZOOM High Resolution Profiles,
  ZOOM MD Fast MD measurement

## Slide 10: Experion MX – Integrated Measurement System
Enhanced measurements and controls
Improve product quality and operational efficiency
  Enhanced Profile Measurement
  Unique, New Quality Sensors
  Advanced Multivariable MD and CD Controls
Easy to Maintain to enhance Operational Reliability and Minimizes Life Cycle Costs
  Modular sensors with Embedded Self diagnostics simplify maintenance
  Predictive and Preventative Maintenance Tools simplify troubleshooting
  Intelligent Sensors with Digital Signal Processing and communication provides easy access for remote expert support
Notes: Experion MX has designed to provide the lowest possible life cycle costs and improved measurement reliability. By enhancing sensor self diagnostics and digital communications,
9

## Slide 11: Experion MX – Profile Accuracy
Enhanced Profile Measurement Response
  4000 Hz signal processing with 16 bit resolution
  1200 mm/sec scan rate with 2 mm resolution
    40-67% faster Profile measurement response vs. 600 mm/sec rate
    Improved Edge measurement
Profile Measurement Stability and Reliability
  Patented Thermal Equalization System
    Profile accuracy thru start-ups and break recoveries
  Integral Head accelerometers and dynamic X,Y,Z sensor
    Continuous head alignment verification and predictive alarming
  Improved environmental sealing for reliability
    Stainless steel beam covers with easily removable side panels
  Life-time Head Carriage Rollers
    Polymer Wear Inserts replaceable as needed
  Improved Drive Reliability
Long-Life Power Track
  Silicon coated Wire Package
    Redundant Ethernet communication
    Easy access for On-line repair and replacement
Notes: Experion MX has designed to provide the lowest possible life cycle costs and improved measurement reliability. By enhancing sensor self diagnostics and digital communications,
10

## Slide 12: Experion MX – Minimizing Life Cycle Costs
New Modular, Intelligent sensor design
  Improved Sensor / Scanner Self-diagnostics
  Reliable Digital power track and remote sensor diagnostic access
  Fast, simple, cost-effective sensor replacement and repair
Each sensor module is equipped with an Ethernet Diagnostic & Data Acquisition Node (EDAQ) that connects via standard Ethernet
  Node provides diagnostic web pages for service personnel
Sensor modules easily slide on via mounting rails to connect to power, cooling, air & communication
  Enables fast removal and replacement of sensor modules to reduce downtime
  Built-in Remote access and tools to speed expert support and system optimization
  No water connections to leak
Notes: Experion MX has designed to provide the lowest possible life cycle costs and improved measurement reliability. By enhancing sensor self diagnostics and digital communications,
11

## Slide 13
Sr90 BW Sensor
Sensors
Notes: Tissue-Overview_v6_090310.pptPower Exec Overview_v2_030310.ppt
8/26/2025
12
Tissue-Overview_v6_090310.pptPower Exec Overview_v2_030310.ppt
8/26/2025

## Slide 14: Basis Weight Sensor Introduction
Beta-particle absorption principle
Designed with high flux geometry (HFG) principles, for best measurement response
Full Range Standardization modifies sensor calibration across the complete operating range
Other features to maximize performance
Backed by strong application expertise, and flexible options with the NEW Experion MX QCS
*Model Q4202-50
*Model Q4202-50
Notes: Basis Weight sensors are designed with a few principles in mind.
(1st bullet) All sensors use beta-particle absorption (not said here is that the selection choice of which beta-isotope is important, it is an application choice).
(2nd) All BW sensors are designed with HFG and Full Range Standardization. They are fundamental design philosophy (like the Ultimate Driving Machine for BMW) for Honeywell’s BW sensor design.
(3rd and 4th) Standardizations occurs every 20 min (default). Calibration occurs infrequently. This is why one wants to take advantage of incremental modification to the calibration curves and constants with an intelligent standardizing technique.

## Slide 15: High Flux Geometry (HFG) Principles
Reduced Source & Receiver Columns Increases Flux 300%
Reduced Air Columns Reduce Air Temperature Change Effects
Application-Matched Sr90 or Krypton85 sources
Source capsule
2 internal standards
“Close geometry”
Air cylinders, no heating from elec. solenoids
Rotating Source
Notes: HFG basic description – put the beta particles as close to the paper specimen as possible. Make sure detection is also close to the opposite side of the transition.
Kr – Q4201-62,-63,-64 – uses a rotating source body. When open, there is no shutter gap distance.
Pm – Q4202-50 – Pm does not need as thick a body, shutter design is ok. But there is no electrical solenoid to cause self induce heating.

## Slide 16: Full-Range Standardization
Background
  Shutter closed
  8 hour intervals
Off-sheet standardize
  Shutter open
  Adjustable interval (20 minutes typical)
Internal standard measurement
Repeatability sample check
Corrects for:
  Background radiation
First-order correction for:
  Source decay
  Electronic drift
   air mass
     barometric pressure
     air temperature
     gap height (Z)
  Dirt buildup on windows
Precisely corrects for response shift with dirt buildup
Built-in performance verification
Notes: In addition to dirt simulation, standardization performs other corrections.

## Slide 17
Micro Wave Moi Sensor
Sensors
Notes: Tissue-Overview_v6_090310.pptPower Exec Overview_v2_030310.ppt
8/26/2025
16
Tissue-Overview_v6_090310.pptPower Exec Overview_v2_030310.ppt
8/26/2025

## Slide 18: Principle of Measurement
Dielectric constants
  Water: 80
  Fiber: 3
Web’s dielectric constant is, therefore, greatly affected by the moisture content
Pure Dielectric Constant is measured
  Not absorption or power loss
1000 to 3000 MHz
Cavity resonators are sensing elements
Frequency shift is measured with extreme accuracy
  Not signal amplitude
Measurement and Reference Frequencies utilized

## Slide 19: Double Resonance
The frequency difference is a measure of the moisture content
Sharp resonance peaks ensure high precision

## Slide 20: Insensitive to Absorption
Minimum sensitivity to sheet composition
Easy and reliable calibration

## Slide 21: Specifications
Measurement Range
Repeatability (2σ)
Accuracy (2σ)
Dynamic Correlation (2σ)
Measurement Spot Size
Related Measurements
2270: 3% 600 gsm H2O
2273: 3% to 1500 gsm H2O
±0.1% absolute moisture
±0.25% absolute moisture or 2% of web moist. (if greater)
±0.5% absolute moisture or 3% web moisture (if greater)
10.2 cm (4 inches)
Basis Weight

## Slide 22: Features and Benefits
High-resolution Measurement on Heavyweight Products
Unaffected by Salts, ΔpH, ΔCarbon Levels in Sheet
No Contaminant Build-up
Unaffected by Moisture Stratification in the Sheet
Long-Term Measurement Accuracy
Accurate Measurement Under Varying Process Conditions
Microwave Frequency Shift Measurement technique
High frequency Microwaves
Non-contacting Design
Dual Resonant Cavity
Automatic Standardization
Dynamic Z, Sheet Temp Sensors

## Slide 23
Micro Wave Moi MD Sensor
Sensors
Active Microwave Sensors
Notes: Tissue-Overview_v6_090310.pptPower Exec Overview_v2_030310.ppt
8/26/2025
22
Tissue-Overview_v6_090310.pptPower Exec Overview_v2_030310.ppt
8/26/2025

## Slide 24: Pre Dryer Moisture MD
The water content at press section is very critical in pulp and paper production process because of his direct influence on the operation of the dryer section with important effects on energy consumption and runnabilty of the machine.
The R1 has superior tolerance to the oscillation/vibration of paper sheet and is completely independent from other sheet properties like color, type of fibers, temperature.
No contact with the sheet is needed and no recalibration needed with grammage production change (virtually maintenance free).
Quality Efficiency Runnability
Notes: Fixed point sensors can be located at many places along the path of the paper machine, including through the dryer sections. Each Sensor Control Cabinet (SCC) can support six sensors.

## Slide 25: Q4215-61 Color Measurement Introduction
10 Hz response:
  L*, a*, b*, FI, Br, Whiteness
  All measurements corrected to infinite-pad reflectance
Color is calculated from measured reflectance spectrum, giving benefit of metamerism analysis
Moving sheet is stabilized using non-contacting vortex sheet control
The effect of dust and dirt buildup on color measurement is mitigated online
Laboratory accuracy
Notes: - Introduction slide
Honeywell’s Color Measurement provides scanning measurements of color and appearance quantities of paper web able to provide profiles and trends of the coloring process.

## Slide 26: Measured variables
Spectral quantities:
  Reflectance R()
  Apparent reflectance R’(|S) for an illuminant S
Derived quantities under defined CIE observer(s) and illuminant(s):
  CIE tristimulus values XYZ
  CIE L*, a*, b* or Hunter L, a, b
  Brightness (ISO,TAPPI, D65)
  Fluorescence index FI
  CIE Whiteness and Tint
As samples of stack or estimated stack measurements on a single layer moving web
X, Y, Z
x, y, z
CIE L*, a*, b*
Hunter L, a, b
Specify: - CIE illuminant
- CIE observer
CIE Whiteness
R()
L* = 0
L* = 100
-b*
+b*
+a*
-a*
Notes: From reflectance (UV excluded measurement) and apparent reflectance for an illuminant S (UV included measurement) any other derived color and apparent quantity can be calculated under specified CIE observer and illuminant.
Q4215 provides most used color and appearance measurements.
Color is measured following ISO standards:
ISO 5631-1 indoor daylight conditions C/2
ISO 5631-2 outdoor daylight conditions D65/10
ISO 5631-3 indoor illumination conditions D50/2
Brightness:
ISO 2470-1 Indoor daylight conditions (ISO brightness)
ISO 2470-2 Outdoor daylight conditions (D65 brightness)
CIE Whiteness:
ISO 11475 outdoor daylight conditions D65/10
ISO 11476 indoor daylight conditions C/2
25

## Slide 27: Q4215 Color Measurement
10 Hz response:
  L*, a*, b*, FI, Br, Wht
  All measurements corrected to infinite-pad reflectance
Color is calculated from measured reflectance spectrum, giving benefit of metamerism analysis
Moving sheet is stabilized using non-contacting vortex sheet control
The effect of dust and dirt buildup on color measurement is mitigated online
Laboratory accuracy
Notes: - Introduction slide
Honeywell’s Color Measurement provides scanning measurements of color and appearance quantities of paper web able to provide profiles and trends of the coloring process.

## Slide 28: Experion MX SW
RAE
RAE
API
API
. . .
. . .
Real-Time Application Environment (RAE)
Real-Time Application Environment (RAE)
Recipe
Recipe
Handling
Handling
Alarm
Alarm
Processing
Processing
Process
Process
Visibility
Visibility
ODX
ODX
OPC
OPC
Sensor
Sensor
Processing
Processing
MD
MD
Control
Control
I18N
I18N
CD
CD
Control
Control
Color
Color
Control
Control
TMMS
TMMS
Core
Core
Notes: Updated 2014.04.07by Antti Paavola.

## Slide 29: Experion MX Application SW
RAE
RAE
API
API
. . .
. . .
Real-Time Application Environment (RAE)
Real-Time Application Environment (RAE)
Recipe
Recipe
Handling
Handling
Alarm
Alarm
Processing
Processing
Process
Process
Visibility
Visibility
ODX
ODX
OPC
OPC
Sensor
Sensor
Processing
Processing
MD
MD
Control
Control
I18N
I18N
CD
CD
Control
Control
Color
Color
Control
Control
TMMS
TMMS
Core
Core
Operator Displays
The Da Vinci Application Software package
provides the operator displays which are
common to all QCS configurations:
The Experion MX Application Software provides the basic application packages for Experion MX Quality Control System (QCS). These applicaton packages build the foundation for QCS measurement subsystem, scanner and sensor support, analysis, reporting, information system and seamless integration to Machine Directional (MD) and Cross Directional (CD) Control applications.
Standard Displays | Analysis Displays | MIS Displays
Limit Alert | Histogram | Reel Display
Recipe Change | Trend Plot | Shift and Day Display
Production Data | SQC Charts | Grade Display
Profiles | Streak Detection | Numeric profile
Data Display | Profile Stability | Report Setup
Multiple Profiles | Histogram | 
High Resolution Profiles | History Trend | 
Quality Summary | Profile Spectrum | 
Trend & Profile | MD Spectrum | 
Multi Fixed Point | Fixed Point Analysis | 
Trend & Fixed Point |  | 
Multi Profile White |  | 

## Slide 30: Experion MX Application SW Display Examples
Profile Display
Trend Plot Display
Reel Display

## Slide 31: Advanced Color Map
Advanced Color Map
The Advanced Color Map display shows fifty scans of data in either a two or three dimensional plot using colors to indicate the amplitude of the data. Additionally, a MD trend and a CD profile can be viewed for any point within the fifty scans. This display is typically used to analyze a series of profile arrays from scanning sensors, but it can be used to plot any array data in the Experion MX system. The color map format makes it easy to spot trends or patterns in the data.

## Slide 32: Profile Spectrum
Profile Spectrum
The Profile Spectrum display shows the frequency power spectrum of any cross direction profile measured by a scanning sensor. The power spectrum highlights dominant spatial frequency components as distinct peaks. This is very useful when trying to determine the source of profile variations or when evaluating cross direction control performance.
MD Spectrum
The MD Spectrum Display shows the frequency power spectrum of any trended (i.e. time based) variable in the Experion MX system. The power spectrum highlights dominant frequency components as distinct peaks. This is very useful when trying to determine the source of machine direction variations or when evaluating machine direction control performance.

## Slide 33: Alarm Handling
Alarm Summary
Process, control and system maintenance alarms are shown on the Alarm Summary display, which has been designed to conform to the Abnormal Situation Management (ASM) Consortium’s recommended guidelines. The Alarm Summary is highly configurable (e.g. custom help text, priority colors, alarm grouping) to ensure that operators are presented with the data they need to focus on the problem at hand. A one line summary (date and time, source, condition, priority, description, etc.) is shown for each alarm as well as an indication of whether or not it has been acknowledged. The Alarm Summary can be quickly accessed by a button on the static toolbar or by clicking on the Alarm Indicator in the status zone. The Indicator turns red when alarms are present and blinks until all alarm conditions are cleared, or the operator acknowledges them.

## Slide 34: HTML5 Web Displays
Notes: Updated 2014.04.07by Antti Paavola.

## Slide 35: HTML5 Web Displays
Zero Install HMI
  Access displays from Web Browser –Chrome, IE without any installation required on client machines.
Multiple Screen and Device Support
  Auto Scale to big size monitors. (55 inch)
  Supports normal monitors / PC station. Touch / Non-touch Screens.
  Support 11” and above Tablet and Pads.
Support for all Paper and CWS segments.

## Slide 36: HTML5: Four Control Template Example

## Slide 37: HTML5: Four Control Template Example

## Slide 38: Extended History

## Slide 39: Extended History
QCS Extended History is
  Simple to Configure
  Integrated with QCS Platform
  Usable for Operators and Engineers
One Year History Supports
  Trend Variables (Scalar Parameters)
  ACM Variable (Array Parameters)
  MIS Reports
It Enables
  Data for engineering and process analysis
  Foundation for quality management system.
EHDB | Total number of Trend Variables (Scalar Values) | 120*
 | Total number of ACM Variables (Array) | 30
 | Total Number of virtual Trends | 120*
 | Minimum Sampling Period in seconds | 5
 | History Support Duration in Year | 1
MIS | Minimum Reel Turn-up Time (In minutes) | 15
 | Total Rolls in a Year | 30,000
* As a special can be extended to support more variables. |  | 

## Slide 40: Historical Data Analysis: Color Map
Enhanced to display up to 400 Scans Data at a time
Enhanced to display up to 400 Scans Data at a time

## Slide 41: Integrated Displays: Trend, MIS, Export Data
Trend Control will show directly the historical data up to last one year.
In MIS one can select one year old Roll for viewing the report.
Export the tag data for offline analysis.

## Slide 42: MD Controls
Dry Weight
Reel
Moisture
Thick Stock
Clay Flow
TiO2 Flow
Steam Pressure
Speed
0
Ash
Opacity
0
0
0
0
0
Notes: Updated 2014.04.07by Antti Paavola.

## Slide 43: Typical Pulp Dryer machine QCS MD Control
MAJOR CONTROL LOOPS SHOWN
5941 De-Coupled
MOISTURE
Steam Loop
SP
5943 DRYER
SHUTDOWN
CONTROL
5940 REEL Dry
WEIGHT
STOCK
Loop
SP
5946 JET/WIRE
CONTROL
TOTAL HEAD
Loop
5961 DRYSTOCK
CONTROL
5947 CO-ORDINATED SPEED
CONTROL
SPEED
Loop
SteamLoop
SP
SP
SP
SP
SP
SP
Scanner
Weight
Moisture
Dry Weight

## Slide 44: Slice Lip/Dilution Control ProFlow II
Notes: Updated 2014.04.07by Antti Paavola.

## Slide 45: What is ProFlow?
A complete dilution profiling actuator solution from Honeywell
Suitable for use with all makes of dilution headboxes
  Compatible with all rotary distributors and linear dilution headers
  Solutions for rotary or linear valve applications
  Mountings available to customer-supplied valves
  Packaged Honeywell solutions can include valves for total supply
Optimum profiles and profitable results assured with Honeywell profile optimizers including Performance CDMultivariable Control

## Slide 46: New ProFlow Design
Optical Encoder
Standard Rotational Valve (up to 1.5”)
One Disconnectable Network Drop Cable with ‘Mini’ Connector (not shown)
DC Stepper Motor
Removable Stainless Steel Housing
Position Indicator on Output Shaft
Designed for 20 Nm output torque, optional upgrade within same housing to 30 Nm at additional cost
Planetary Gear
Fixed Internal Mechanical Stops (not shown)
One per Actuator Internal CDConnect Module

## Slide 47: Adaptive Alignment
Notes: Updated 2014.04.07by Antti Paavola.

## Slide 48: Adaptive Alignement Features
After commissioning CD control performances are continuously monitored to detect any changes in actuator’s alignment
If a reduction in control performance is detected the actuator alignment is checked in the background while the CD controls continue to operate as normal.
Alignment parameters can be deployed automatically, or only with the Operator approval

## Slide 49: Identification
Executes an intelligent, closed loop, Pseudo-Random Binary Sequence (PRBS) perturbation which adapts to process conditions.
The magnitude, location, and duration
of the PRBS are determined automatically
based on the process dynamics,
CD actuator setpoints and constraints.
  Induces less CD variation than a
  traditional bump test.
If the resulting process model is rated as “Good” the new alignment is deployed. Otherwise, the PRBS is redesigned and repeated

## Slide 50: Picketing due to Misalignment

## Slide 51: Devronizer Steambox
Notes: Updated 2014.04.07by Antti Paavola.

## Slide 52: Steambox and Hot Pressing Theory
Profiling systems introduce a temperature profile into the web in the cross direction (CD)
To be effective, temperature profile must get to a press nip(s) OR water removing vacuum boxes
At the same nip pressure, more water is removed from hot areas than from cold areas due to lower water viscosity and surface tension
One kilogram of condensing steam will release 2257 kJ of energy and heat 100 kg of water by 5.6ºC
Heat reduces limitations to water removal to accomplish
  Dewatering by hot pressing
  CD moisture profiling
Each 10ºC (18ºF) increase in web temperature increases sheet dryness into the dryers by 1% yielding
  5% speed up or…
  5% dryer load reduction
30C (54F) bump response by Devronizer measured after the press!!

## Slide 53: Devronizer Operation
All steam applied is controlled by the XP10 for maximum profiling range
  Profiling steam is fully separated from zone to zone
Actuator inserts completely into steam header
  Reduced cross section enables location in tighter press sections than other steamboxes
  Prevents condensation of steam within actuator
Formed cross section ensures stronger, lighter beam with minimal beam deflection
Designed to stay Clean
Optimum steam delivery, close to the sheet
  Narrow and precise profiling response
  Prevents boundary layer turbulence to mix the profiling steam
The patented screen plates are custom designed to distribute steam evenly at the optimum, application-matched velocity and are engineered to prevent fibers from entering the Devronizer
Flush face
  Limits boundary air
  Limits fiber collection
  Easy to clean
Dynamic
Steam Curtain
Notes: Vanhat kuvat. Muuta. Vain yksi stage

## Slide 54: Devronizer Features
Flush-mounted, patented removable screen plates
  Designed to stay clean
  Mirror finish option available effectively preventing dirt buildup
  Alternate materials of construction available (AL 904L, 254-SMO, AL-6XN) for extreme environments
Adjustable edge deckles
  Installed as standard on all Devronizers
  Adjustable while machine is running
Advanced condensate removal system guarantees drip-free operation with properly conditioned steam
  Condensate removal is provided for all internal chambers
  Internally-heated anti-drip edges prevent external condensate dripping
  Steam heated evacuation ducts available as an option where there is risk of condensation on other equipment
Various retraction options available
Notes: Number 4 mirror finishing.

## Slide 55: XP10 Actuator – Ultimate Reliability
Requires no maintenance
  Designed to last the life of the Devronizer
  No elastomers or internal seals
  Completely welded assembly
Sealed to atmosphere
  Impossible to leak or drip from internal condensation
Frictionless Design
  Negligible hysteresis for improved profile control
  Increased flow range
  High resolution
Backed by a 15-Year Warranty
Maintenance Free
Corrosion Resistant
Free of Electronics
Free of Elastomers
Frictionless Motion
ROBUST AND RELIABLE
Notes: Add XP10/2

## Slide 56: Devronizer System With Intelligent IDP Control
Power/CDWeb Network LON
IDP Control Cabinet
CDWeb Manager
Air Signal 6-30 PSI (30-200 kPA)
Steam Control Unit,SCU (Optional)
Controlled Steam Supply (Flexible Steam Hose)
CDWeb
Explorer &
IDP Scout (optional)
Supervisory Protocols:
Ethernet: OPC, Modbus TPC, ODX
Serial: Modbus RTU, SCL
Link to QCS
IDP2 Modules
Outputs control pressure for up to 8 profiling actuators
Fast response reacts immediately to set point changes
Control resolution <0.5%
IDP2 module recognizes leaks and compensates intelligently:
  assign higher priority to a zone, minimizing the effects of small leaks
  generate diagnostic alarms for easier maintenance planning
Ethernet
Instrument Air 60 PSI
(400 kPA)

## Slide 57: Devronizer Benefits
ROI typically less than 6 months!
Value
Quality and Efficiency
Increase production 5-15% if dryer limited
Reduce fiber consumption
Increase reel moisture targets
Reduced steam usage in dryer section
Increase machine efficiency
Less sheet breaks, less rejects
Increased felt life
30–80% reduction in CD moisture variation
Improved sheet consolidation and strength
Reduced dryer picking
Improved sheet smoothness
Reduced sheet stresses and tension caused by uneven drying
Improved caliper profiles and reel build
Improved runnability
Improve downstream operations
  Calendering, coating, winding, converting and printing
More than 1800 Devronizers delivered covering all grades and all applications

## Slide 58: Q&A
End of Session
Any Questions?
Notes: Multiple Teams
DCS Vendor, PLC Vendor, EPC, Customer
Extensive co-ordination
  Data exchange, System setups, Testing, Troubleshooting
Higher Risk
  Schedule risk , Rework, Low Reliability
  Inconsistent operator interface
  Higher training expenses
Few Teams
One DCS & PLC Vendor, Customer
Less co-ordination
  Few teams, Access to system knowledge, Faster system setup, testing and troubleshooting
Low Risk
  Reduced elements to manage, Single point of responsibility
Consistent operator interface
Lower Training Expenses