## Slide 1: Experion mx Q6088 compact scanner
Johann Resl
Notes: v5 December 18, 2024

## Slide 2: Q6088 Overview
The Q6088 Compact Scanner provides high measurement performance, low maintenance, and environmental protection for long-term 24x7 reliability—all in a compact and economical form factor.

## Slide 3: Q6088 Overview
Leveraging five decades of Honeywell experience in the harsh paper machine environment, it is the right scanner for production lines where space is at a premium.
Designed to meet the needs of applications requiring only one or two scanning sensors:
  Tissue: Fiber Weight & Moisture + Crepe
  Board: Moisture + Basis Weight
  Coating: Top & Bottom Coat Weight

## Slide 4: Q6088 benefits
Small machine direction footprint
  25% narrower than Honeywell’s previous O-frame paper scanners
Drive system with two decades of proven reliability
Sensor signal processing and communications based on the Ethernet Data Acquisition (EDAQ) architecture introduced in 2010 with the flagship Experion MX Q4000-80 scanner
  Internal Measurement Support System (MSS), no remote cabinet
  Ethernet in power track
  Supports the latest MXIR moisture, fiber weight, and coat weight sensors
  Advanced scanner and sensor diagnostics

## Slide 5: Q6088 benefits
Environmentally protected against heat, humidity, and dust
  Beam purge & seals
  Air wipe “sneeze” & head gap cleaner
Industrial Internet of Things (IIoT) ready for use with Honeywell’s QCS 4.0 remote performance monitoring
  Analytical software and remote expertise reduces cost of ownership

## Slide 6: Q6088 features - FrAme
Cross beams and end supports are custom engineered, extruded, aluminum U-beams
Extruded aluminum head carriage tracks are precisely aligned and bonded in place to upper and lower beams
Track alignment cannot degrade over time

## Slide 7: Q6088 features – environmental
Purge Air Inlet
Purge Air Inlet
Heat Exchanger
Beam Seals
Beam Seals

## Slide 8: Q6088 features – environmental
Purge Air
Pressurizes frame to keep dust out
Beam Seals
Co-extruded rubber/polyethylene flaps which prevent ingress of material into the track. Seal remains closed until guide wheels on carriage push it open as the head moves.
Heat Exchanger
Cools endbell electronics and drive system

## Slide 9: Q6088 features – Cable End
The drive system and all electronics are housed in the insulated and cooled endbell
Frame controller and measurement support system are the same as used in other Honeywell scanner models
Common spare parts for multiple scanners
Swing out doors provide full access to all components

## Slide 10: Q6088 features – Cable End
Frame Controller
Measurement Support System Computer
DC Motor
Drive Shaft Access Panel
Swing Out Panel
Left Side
Right Side
Power Track Entrance
End View
Circulation Fan
Heat
Exchanger
Fans

## Slide 11: Q6088 features – Distant End
Compressed Air Tank for head gap cleaning
56V Transformer for heating air wipe
Idler Pulley & Drive Belt

## Slide 12: Q6088 features – head
Standard (single sensor) and Extended (two sensor) heads available
All scanners are made long enough to accommodate an Extended head to support adding a second sensor in the future
Environmentally protected against dust and water ingress with internal temperature control
Sensors utilize Honeywell’s Ethernet Data Acquisition (EDAQ) architecture for communication to Experion MX server

## Slide 13: Q6088 features – head
Standard Head
CD Extended Head
MD Extended Head

## Slide 14: Q6088 features – head
Heated Air Wipe with Static Eliminator
Air Supply
Air Supply
Head
Cover
Latches
EDAQs
Heat Exchangers

## Slide 15: Q6088 features – head
Air / Water
Entrance
Power Track
Entrance
+/-18 degree
Pass Angle

## Slide 16: Q6088 Sensors
Q4303-5x Basis Weight, Sx18, Kr85 (Low, Medium, High Ash)
Q4303-54 Basis Weight, Sx18, Sr90
Q6405-50 MXIR Moisture
Q6405-60 MXIR Fiber Weight & Moisture
Q6240-60 MXIR Opacity
Q6406-xx MXIR Coat Weight
Q6224-70 Crepe
Microwave moisture, color and other sensors also available

## Slide 17: Q6088 options
Q6735-00 Outboard Edge Detect
Q6750-00 Head Gap Cleaner
Q6760-00 Calibration Sample Holder

## Slide 18: Q6088 specifications
Category | Specification
Maximum Sheet Width | 6000 mm [236 in]
Passline Height | 654 mm [25.7 in] from top of mounting pad
Passline Angle | Up to ± 18° for Q6088-10/-20, ± 1° for Q6088-25
Drive System | DC motor: 24VDC, 9A, 0.15 kW [0.2 hp]
Head MD Dimension | 343 mm [13.5 in] or 613mm [24.1 in] including air wipe
Sensor Signal Digitization | 4kHz sampling with 1200 Hz 1st order filter
Signal Resolution | 16 bits averaged, with oversampling
Scan Speed | 50 - 600 mm/s [2 - 24 in/s]
Head Positioning Accuracy | ± 1 mm [0.04 in]
Profile resolution | 2–5 mm [0.08–0.20 in] databoxes across full web width
Communication | Ethernet, TCP/IP protocol
Max Temp at End Supports | 65ºC [150ºF]
Max Temp on Sheet | 65ºC [150ºF] measured 150mm [6”] from the sheet
Relative Humidity On Sheet | Up to 95% (non-condensing)
Electrical Power | 208-240 Volts AC, 15A nominal, 50/60 Hz, single phase

## Slide 19: Scanner comparison
 | Q6088 | Q4022-34 | Q4000-80
Application | Paper machines with basic measurement needs | Paper machines with moderate measurement needs | Premium scanning platform for all paper making applications
Beam Material | Extruded Aluminum | Steel | Extruded Aluminum
Beam Design | U-Beam | I-Beam | Box Beam
Max Sheet Width | 6.0 m [236 in] | 6 m [236 in] | 10 m [396 in]
MD Head Width | 343 mm [13.5 in] 613 mm [24.1 in] | 467 mm [18.3 in] | 460 mm [18.1 in] 645 mm [25.4 in]
Internal Sensors | 1 or 2 | 4 | 4 or 6
External Sensors | 0 | 1 | 2 or 4
Max Scan Speed | 600 mm/s [24 in/s] | 406 mm/s [16 in/s] | 1200 mm/s [48 in/s]
EDAQ / Ethernet | All Sensors | Only MXIR Moisture | All Sensors
MSS Location | Cooled Endbell | Remote Universal PMP | Cooled Endbell
Advanced Diagnostics | No | No | Yes
Maintenance Scheduling | No | No | Yes

## Slide 20: Q6088 Model NUmbers
Scanner
Q6088-10 Compact O-Frame Scanner, Standard Head (1 sensor)
Q6088-20 Compact O-Frame Scanner, CD Extended Head (2 sensors)
Q6088-25 Compact O-Frame Scanner, MD Extended Head (2 sensors)
Q6088-MM Trim width in MM
The -10 will be built long enough to accommodate a CD Extended Head so a second sensor can be added in the future
Q6088-10
Q6088-25

## Slide 21: Q&A
Any questions?